## Slide 1: STEEL CEP
SCHEME 1

## Slide 2: Group Members
Adnan Haider
Ahmad Shah
Ahmed Ebadullah
Ahmer Naseer
Alamzaib Qureshi
Ali Ahmed
Ameer Hamza
Ammar Akhtar Goraya
Fahad Nasir Mughal
Haider Taseer Khan
Hammas Zubair
Husnain Kabir
Hassan Ahmad Khan
Irtaza Badar
Khizer Aamer
Mukarim Ali Syed

## Slide 3: Contents
Problem Statement | 4
Initial Thoughts | 5
Assumptions | 6
Introduction | 7
Client Requirements | 8
Loads & Combinations | 9
Plans & Sections | 12
Scheme Sketches | 17
Modelling | 18
Recommendations | 19

## Slide 4: Problem Statement
A multi-national polythene manufacturer’s factory
Factory to be clad with profiled steel sheet sandwich panels
50% roof lighting
Several checks such as secondary bending and local buckling of the truss member walls omitted.
A design appraisal need to be prepared with:
  Appropriate sketches
  Functional framing
  Load transfer
  Serviceability
  Stability aspects

## Slide 5: Initial Thoughts
3 available schemes to complete this task
We are using Scheme 1
Consists of:
  1 central column,
  Primary & secondary trusses
  Lateral & elevation bracing
Modelling done in SAP 2000
Checked for deformations

## Slide 6: Assumptions
The following assumptions have been made for ease of modelling:
  The ground is level across site
  Access for all types of vehicles is adequate
  Site has sufficient storage place
  Existing buildings are far away
  Ground conditions are constant across the site
  Bracing is allowed on external elevations
  Bracing is allowed on roof

## Slide 7: Introduction
The structure contains 2 systems:
Gravity System which consists of:
  Primary Truss
  Secondary Truss
  Central Column
  Edge Columns
Lateral System which consists of:
  Lateral Roof Bracing
  Elevation Bracing
Additional cladding on all sides

## Slide 8: Client Requirements
200 ft. square, single storey factory
Only one central column allowed
One large sliding door opening 16ft. high
Minimum clearance inside the building of 20.ft
Structure has no windows

## Slide 9: Loads
Live load (L.L):
Roof snow load: 0.75 kN/m2
Factory roof services: 0.65 kN/m2
Dead load (D.L):
Cladding load: 0.30 kN/m2
Steel load: 0.20 kN/m2
Wind load (W.L):
Wind load: 2.0 kN/m2

## Slide 10: Load Combination:
1.2 D.L + 1.6 L.L (we will use this combination)
1.4 D.L
0.9 D.L + 1.0 W.L
1.0 D.L + 1.0 L.L (Fn)

## Slide 11: Load Calculations
L.L = (0.75+0.65) x 21 = 29.4 Psf
D.L = (0.30+0.20) x 21 = 10.5 Psf
W.L = 2.0 x 21 = 42 Psf
Factored Load = 1.2 D.L + 1.6 L.L
= 1.2 (10.5) + 1.6 (29.4)
= 59.64 Psf ≈ 60.0 Psf

## Slide 12: Plan View

## Slide 13: Sections
Primary Truss

## Slide 14: Sections
Secondary Truss

## Slide 15: Load Path

## Slide 16: 3D view
Lateral system

## Slide 17: Scheme Design

## Slide 18: Software Model

## Slide 19: Recommendations
The advantages of using Scheme 1 are as follows:
  Central Column will reduce internal loads and moments on structure
  Less chances of deflection
  Less steel involved as less dead load of structure
  Less load running into foundation, as load is well distributed

## Slide 20: Contd.
The dis-advantages of using Scheme 1 are as follows:
  Central Column takes up space
  Lots of primary connections – dangerous in case of seismic activity